## Slide 1: Starting Workflow – Project Interdependencies
Having a working P1: PowerFlow code is a prerequisite for a couple of other tasks: (P4: StateEstimation, P5: OptimalPowerFlow). NRPF only though.
P3: ContinuationPowerFlow does NOT require the full implementation of P1, and can be done in parallel. Some functions from P1 are required though.
Only P2: SparsePowerFlow is a completely independent task, and can be done in parallel. In fact it is not permissible to use any assets from the other projects.
Once P1 is completed ALL other projects can be completed in parallel, i.e P2, P3, P4 and P5 do NOT have any interdependencies.

## Slide 2: Starting Design Decisions
A SINGLE main file, from where Dr. Noel can be shown all five projects with just a few clicks. This file should only contain meta information, like user defined variables. E.g. whether to plotResults, show yBus, save Jacobians, plotCPF curves, which is the chosen CPF bus, showing some symbolic formulae, saving tables, etc.
Use DataFrames (tables) for busData, branchData (and a handful of other results). For convenient data retrieval, good visualization.
Write functions in modules. Modules can be NKGPowerFlow, NKGSparsePowerFlow, NKGContinuationPowerFlow, NKGStateEstimation and NKGOptimization. Unlike MATLAB where it is standard to write a single function in a single .m/.mlx file and just addpath the address of all the functions.
Many (smaller) functions instead of grand scripts.
If you have to scroll too much to check a bug in your script, your script could probably use some refactoring.
Try to commit and push your code whenever you feel that your code is:
  1) Even slightly, but tangibly different in its current state compared to its previous state*
  2) It runs correctly and hasn’t altered any previous correct results*.
  * It’s not possible to follow these rules every time, but do minimize such exceptions.

## Slide 3: Sample functions in modules
NKGPowerFlow
  constructYBus
  solveUsingPowerFlow: NRPF/FDPF We can make it work for both powerFlowMethods: “NRPF” or “FDPF”.
    initializeVectors: Handy function which reads [busData, branchData] and can retrieve highly used parameter values like listOfPVBuses, nPQ, PSpecified, etc.
    computeBusInjections: calculate P_i and Q_i
    computeMismatches: NRPF/FDPF a simple function which calculates mismatches (for every Powerflow iteration) by first computing power injections. Helpful in creation of diagonal Jacobian elements too.
    constructJacobian: NRPF/FDPF Compute J11, J22 (and J12, J21 and J in case of NRPF)
    solveUsingLU: Using given Jacobian (J11/J) and mismatch vector (delP/[delP; delQ]), compute correction vector (delDelta/[delDeltas; delV]).
      solveUsingForwardSubstitution
      solveUsingBackwardSubstituion
  displayPowerFlowResults: A neat table containing [V, delta, P, Q] with easy to see rows called as ‘Bus 01’, ‘Bus 02’ …
  plotPowerFlowResults: Compare your own results to the results in the CDF file ,via two plots: Relative percentage difference in pu Voltages and absolute difference in delta values.

## Slide 4: Sample functions in modules
NKGContinuationPowerFlow
  Dependencies: NKGPowerFlow: initializeVectors, computeBusInjections, solveUsingLU

## Slide 5: Sample functions in modules
NKGOptimalPowerFlow
  constructYBus
  solveUsingPowerFlow: We can make it work for both powerFlowMethods: “NRPF” or “FDPF”.
    initializeVectors: Handy function which reads [busData, branchData] and can retrieve highly used parameter values like listOfPVBuses, nPQ, PSpecified, etc.
    computeMismatches: a simple function which calculates mismatches (for every Powerflow iteration) by first computing power injections.
    constructJacobian: Compute J11, J22 (and J12, J21 and J in case of NRPF)
    solveUsingLU: Using given Jacobian (J11/J) and mismatch vector (delP/[delP; delQ]), compute correction vector (delDelta/[delDeltas; delV]).
      solveUsingForwardSubstitution
      solveUsingBackwardSubstituion

## Slide 6
Have the GitHub Desktop app installed.
Have MATLAB installed. It helps to visualize desired outputs and check for function input arguments and outputs.
Clone my repo

## Slide 7
ReadCDF [Skipped]
busData [14 x 18 table]
branchData [20 x 15 table]
N = 14
numBranch = 18
[PSpecified, QSpecified, V, delta, ...
listOfPQBuses, listOfPVBuses, nPQ, nPV, ...
listOfNonSlackBuses] = initializeVectors(busData, MVAb);
[P, Q, V, delta] = solveForPowerFlow(PSpecified, QSpecified, V, delta, ybus, BMatrix, E, nPQ, nPV, listOfPQBuses, listOfNonSlackBuses, numIterations, toleranceLimit, powerFlowMethod);

## Slide 8
[P, Q, V, delta] = solveForPowerFlow(PSpecified, QSpecified, V, delta, ybus, BMatrix, E, nPQ, nPV, listOfPQBuses, listOfNonSlackBuses, numIterations, toleranceLimit, powerFlowMethod, displayTables, printJacobians, printMismatches, printPowerFlowConvergenceMessages);