## Slide 1: Starting Workflow
Having a working P1: PowerFlow code (NRPF only for all other tasks) is mostly a prerequisite for most other tasks (P3: ContinuationPowerFlow, P4: StateEstimation, P5: OptimalPowerFlow).
Only P2: SparsePowerFlow is an independent task. In fact it is not permissible to use any assets from the other projects.

## Slide 2: Starting Design Decisions
Use DataFrames (tables) for busData, branchData (and a handful of other results). For convenient data retrieval, good visualization.
Write functions in modules. Modules can be NKGPowerFlow, NKGSparsePowerFlow, NKGContinuationPowerFlow, NKGStateEstimation and NKGOptimization. Unlike MATLAB where it is standard to write a single function in a single .m/.mlx file.

## Slide 3: Sample functions in modules
NKGPowerFlow
  solveUsingPowerFlow: We can make it work for both powerFlowMethods: “NRPF” or “FDPF”.
    initializeVectors: Handy function which reads [busData, branchData] and can retrieve highly used parameter values like listOfPVBuses, nPQ, PSpecified, etc.
    computeMismatches: a simple function which calculates mismatches (for every Powerflow iteration) by first computing power injections.
    constructJacobian: Compute J11, J22 (and J12, J21 and J in case of NRPF)
    solveUsingLU: Using given Jacobian (J11/J) and mismatch vector (delP/[delP; delQ]), compute correction vector (delDelta/[delDeltas; delV]).
      solveUsingForwardSubstitution
      solveUsingBackwardSubstituion

## Slide 4
Have the GitHub Desktop app installed.
Have MATLAB installed. It helps to visualize desired outputs and check for function input arguments and outputs.
Clone my repo

## Slide 5
ReadCDF [Skipped]
busData [14 x 18 table]
branchData [20 x 15 table]
N = 14
numBranch = 18
[PSpecified, QSpecified, V, delta, ...
listOfPQBuses, listOfPVBuses, nPQ, nPV, ...
listOfNonSlackBuses] = initializeVectors(busData, MVAb);
[P, Q, V, delta] = solveForPowerFlow(PSpecified, QSpecified, V, delta, ybus, BMatrix, E, nPQ, nPV, listOfPQBuses, listOfNonSlackBuses, numIterations, toleranceLimit, powerFlowMethod);

## Slide 6
[P, Q, V, delta] = solveForPowerFlow(PSpecified, QSpecified, V, delta, ybus, BMatrix, E, nPQ, nPV, listOfPQBuses, listOfNonSlackBuses, numIterations, toleranceLimit, powerFlowMethod, displayTables, printJacobians, printMismatches, printPowerFlowConvergenceMessages);