## Slide 1: Starting Workflow
Having a working P1: PowerFlow code (NRPF only for all other tasks) is mostly a prerequisite for most other tasks (P3: ContinuationPowerFlow, P4: StateEstimation, P5: OptimalPowerFlow).
Only P2: SparsePowerFlow is an independent task. In fact it is not permissible to use any assets from the other projects.

## Slide 2: Starting Design Decisions
A SINGLE main file, from where Dr. Noel can be shown all five projects with just a few clicks. This file should only contain meta information, like whether to plotResults, show yBus, Jacobians, plotCPF curves, chosen CPF bus, showing some symbolic formulae, saving results, etc.
Use DataFrames (tables) for busData, branchData (and a handful of other results). For convenient data retrieval, good visualization.
Write functions in modules. Modules can be NKGPowerFlow, NKGSparsePowerFlow, NKGContinuationPowerFlow, NKGStateEstimation and NKGOptimization. Unlike MATLAB where it is standard to write a single function in a single .m/.mlx file.

## Slide 3: Sample functions in modules
NKGPowerFlow
  constructYBus
  solveUsingPowerFlow: NRPF/FDPF We can make it work for both powerFlowMethods: “NRPF” or “FDPF”.
    initializeVectors: Handy function which reads [busData, branchData] and can retrieve highly used parameter values like listOfPVBuses, nPQ, PSpecified, etc.
    computeBusInjections: calculate P_i and Q_i
    computeMismatches: NRPF/FDPF a simple function which calculates mismatches (for every Powerflow iteration) by first computing power injections.
    constructJacobian: NRPF/FDPF Compute J11, J22 (and J12, J21 and J in case of NRPF)
    solveUsingLU: Using given Jacobian (J11/J) and mismatch vector (delP/[delP; delQ]), compute correction vector (delDelta/[delDeltas; delV]).
      solveUsingForwardSubstitution
      solveUsingBackwardSubstituion

## Slide 4: Sample functions in modules
NKGContinuationPowerFlow
  Dependency: NKGPowerFlow, for functions: initializeVectors, computeBusInjections,
  solveUsingPowerFlow: NRPF/FDPF We can make it work for both powerFlowMethods: “NRPF” or “FDPF”.
    initializeVectors: Handy function which reads [busData, branchData] and can retrieve highly used parameter values like listOfPVBuses, nPQ, PSpecified, etc.
    computeBusInjections: calculate P_i and Q_i
    computeMismatches: NRPF/FDPF a simple function which calculates mismatches (for every Powerflow iteration) by first computing power injections.
    constructJacobian: NRPF/FDPF Compute J11, J22 (and J12, J21 and J in case of NRPF)
    solveUsingLU: Using given Jacobian (J11/J) and mismatch vector (delP/[delP; delQ]), compute correction vector (delDelta/[delDeltas; delV]).
      solveUsingForwardSubstitution
      solveUsingBackwardSubstituion

## Slide 5: Sample functions in modules
NKGOptimalPowerFlow
  constructYBus
  solveUsingPowerFlow: We can make it work for both powerFlowMethods: “NRPF” or “FDPF”.
    initializeVectors: Handy function which reads [busData, branchData] and can retrieve highly used parameter values like listOfPVBuses, nPQ, PSpecified, etc.
    computeMismatches: a simple function which calculates mismatches (for every Powerflow iteration) by first computing power injections.
    constructJacobian: Compute J11, J22 (and J12, J21 and J in case of NRPF)
    solveUsingLU: Using given Jacobian (J11/J) and mismatch vector (delP/[delP; delQ]), compute correction vector (delDelta/[delDeltas; delV]).
      solveUsingForwardSubstitution
      solveUsingBackwardSubstituion

## Slide 6
Have the GitHub Desktop app installed.
Have MATLAB installed. It helps to visualize desired outputs and check for function input arguments and outputs.
Clone my repo

## Slide 7
ReadCDF [Skipped]
busData [14 x 18 table]
branchData [20 x 15 table]
N = 14
numBranch = 18
[PSpecified, QSpecified, V, delta, ...
listOfPQBuses, listOfPVBuses, nPQ, nPV, ...
listOfNonSlackBuses] = initializeVectors(busData, MVAb);
[P, Q, V, delta] = solveForPowerFlow(PSpecified, QSpecified, V, delta, ybus, BMatrix, E, nPQ, nPV, listOfPQBuses, listOfNonSlackBuses, numIterations, toleranceLimit, powerFlowMethod);

## Slide 8
[P, Q, V, delta] = solveForPowerFlow(PSpecified, QSpecified, V, delta, ybus, BMatrix, E, nPQ, nPV, listOfPQBuses, listOfNonSlackBuses, numIterations, toleranceLimit, powerFlowMethod, displayTables, printJacobians, printMismatches, printPowerFlowConvergenceMessages);