## Slide 1: Dynamic Programming for Power Systems
Aryan Ritwajeet Jha
Notes: Remember to hit the reset button to make sure all the page elements react properly.
There are 20 different layouts that you can choose from.

## Slide 2: Contents
Anamika Dubey and Surya Santoso (2015) Electric Vehicle Charging on Residential Distribution Systems: Impacts and Mitigation.
Problem Statements where Dynamic Programming is utilized.

## Slide 3: Electric Vehicle Charging on Residential Distribution Systems: Impacts and Mitigation Anamika Dubey and Surya Santoso (2015)
Context:
Charge M vehicles (loads) during night-time from M charging stations (nodes).
  Night-time = 6PM to 6AM.
Charge them fully before the next morning.
  They aren’t leaving before 6AM, so no need to optimize the charging timings themselves.

## Slide 4: Electric Vehicle Charging on Residential Distribution Systems: Impacts and Mitigation Anamika Dubey and Surya Santoso
Objective:
minimize cost of the total charging, here taken as Voltage Variability
Design objective (constraint): Charge every EV fully by time T.

## Slide 5: Electric Vehicle Charging on Residential Distribution Systems: Impacts and Mitigation Anamika Dubey and Surya Santoso
NOT an Objective:
No optimization of time intended; every EV plugged in for the full time period from zero to T anyway.

## Slide 6: Electric Vehicle Charging on Residential Distribution Systems: Impacts and Mitigation Anamika Dubey and Surya Santoso
Design Formulation:
Battery-charger power levels P(t) variable only in discrete-steps.
Power-flow-analysis also done in discrete time-steps.
We’re solving a discretized Optimal Control Problem.

## Slide 7: Do we even need a dynamic programming formulation in Power Systems?
Instead of using dynamic programming and optimization on
N state variables (including memory elements like Battery SOC)
C constraints for T time steps
Why not just form:
N*T state variables (including Battery SOC)
C*T constraints plus T additional constraints to maintain continuity for those memory elements. (Let’s assume just one battery in our whole grid)
All into one big ‘steady-state-like’ Optimization problem and plug it into a solver?

## Slide 8: Do we even need a dynamic programming formulation in Power Systems?
Instead of using dynamic programming and optimization, why not just incorporate more state variables, more constraints (both by a factor of the number of time-steps: T) into one big ‘steady-state-like’ Optimization problem and plug it into a solver?
I do not have an answer for this now, I’d imagine that the time complexity will increase exponentially, but that’s just my speculation.

## Slide 9: References (not in order)
CTU Prague Optimal and Robust Control - L5.1 - Introduction to dynamic programming and its application to discrete-time optimal control
The Julia Programming Language - Dynamic Programming and Seam Carving | MIT Computational Thinking Spring 2021 | Lecture 6
Hu et al. (2016) - A Dynamic Programming based method for optimizing power system restoration with high wind power penetration
Guerrero, Heydt et al (2008) - Optimal Restoration of Distribution Systems Using Dynamic Programming
Anamika Dubey, Surya Santoso (2015) - Electric Vehicle Charging on Residential Distribution Systems: Impacts and Mitigations
freeCodeCamp.org - Dynamic Programming - Learn to Solve Algorithmic Problems & Coding Challenges
Johan Driesen et al (KU Leuven, 2009) - The Impact of Charging Plug-In Hybrid Electric Vehicles on a Residential Distribution Grid