## Slide 1: EE 521 Analysis of Power Systems In Julia
Aryan Ritwajeet Jha
Ninad Kiran Gaikwad
Sajjad Uddin Mahmud

## Slide 2: Starting Workflow – Project Interdependencies
Having a working P1: PowerFlow code is a prerequisite for a couple of other tasks: (P4: StateEstimation, P5: OptimalPowerFlow). NRPF only though.
P3: ContinuationPowerFlow does NOT require the full implementation of P1 solveForPowerFlow, and can be done in parallel. Some functions from P1, including construction of Jacobian, are required though.
Only P2: SparsePowerFlow is a completely independent task, and can be done in parallel. In fact it is not permissible to use any assets from the other projects.
Once P1 is completed ALL other projects can be completed in parallel, i.e P2, P3, P4 and P5 do NOT have any interdependencies.

## Slide 3: Starting Design Decisions
A SINGLE main file, from where Dr. Noel can be shown all five projects with just a few clicks. This file should only contain meta information, like user defined variables. E.g. whether to plotResults, show yBus, save Jacobians, plotCPF curves, which is the chosen CPF bus, showing some symbolic formulae, saving tables, etc.
Use DataFrames (tables) for busData, branchData (and a handful of other results). For convenient data retrieval, good visualization.
Write functions in modules. Modules can be NKGPowerFlow, NKGSparsePowerFlow, NKGContinuationPowerFlow, NKGStateEstimation and NKGOptimization. Unlike MATLAB where it is standard to write a single function in a single .m/.mlx file and just addpath the address of all the functions.

## Slide 4: Starting Design Decisions
NO Global Variables – Anything required by a function should either be defined in the function OR be packed into the function as an argument.
Clearly define the data structures going into and out of a function. It is important that we agree on the same data structures (2d-arrays or DataFrames, strings or numerals, etc.) for maximum compatibility and code reusability.
Document those data structures. In Julia it is easy to do so just by putting your documentation in triple grave accents (```). Your documentation will show up whenever a developer hovers their mouse over a function call.

## Slide 5: Starting Design Decisions
Many (smaller) functions instead of grand scripts.
If you have to scroll too much to check for a bug in your script, your script could probably use some refactoring.
Reuse your functions as much as possible.
Try to commit and push your code whenever you feel that your code is:
  1) Even slightly, but tangibly different in its current state compared to its previous state*
  2) It runs correctly and hasn’t altered any previous correct results*.
  * It’s not possible to follow these rules every time, but do minimize such exceptions.

## Slide 6: Starting Design Decisions
Question: Numerical parameters specific to an algorithm, like toleranceLimit, maxIterations for NRPF in P1, CPFItrMax, SectionItrMax, sigma1, 2 and 3 for P3, and so on.. which are NOT gonna be changed or altered by a Dr. Noel: Should they be
  1. hidden from a user away in the function?
    Pros:
      Cleaner, more scrollable main file, functions have reduced input arguments.
    Cons:
      Can get annoying to change parameter values every time by going into a specific function/module during initial development
  Or 2. should they be tinkerable in the main file itself? (this is what I did)
    Pros:
      Highly tinkerable code making way for easier development time.
      The user operating the code via the main file feels truly powerful.
    Cons:
      Number of function arguments gets nasty for some complex algorithms
      Bigger main file. Parameters can feel out of place if the user is NOT interested in running a particular project at the time.

## Slide 7: Sample functions in modules
P1: NKGPowerFlow
  constructYBus
  solveUsingPowerFlow: NRPF/FDPF We can make it work for both powerFlowMethods: “NRPF” or “FDPF”.
    initializeVectors: Handy function which reads [busData, branchData] and can retrieve highly used parameter values like listOfPVBuses, nPQ (#PQ Buses), PSpecified, etc.
    computeBusInjections: calculate P_i and Q_i
    computeMismatches: NRPF/FDPF a simple function which calculates mismatches (for every Powerflow iteration) by first computing power injections. Helpful in creation of diagonal Jacobian elements too.
    constructJacobian: NRPF/FDPF Compute J11, J22 (and J12, J21 and J in case of NRPF)
    solveUsingLU: Using given Jacobian (J11/J) and mismatch vector (delP/[delP; delQ]), compute correction vector (delDelta/[delDeltas; delV]).
      solveUsingForwardSubstitution
      solveUsingBackwardSubstituion

## Slide 8: Sample functions in modules
P1: NKGPowerFlow (contd.)
  displayPowerFlowResults: A neat table containing [V, delta, P, Q] with easy to see rows called as ‘Bus 01’, ‘Bus 02’ …
  plotPowerFlowResults: Compare your own results to the results in the CDF file, via two plots:
    Relative percentage difference in pu Voltages
    absolute difference in delta values.
Caveat: Bus Switching is optional for evaluation, though in general not implementing it for bigger systems will lead to incorrect outcomes or even divergence.

## Slide 9: Sample functions in modules
P2: NKGSparsePowerFlow
Need to rethink all implementations (check Caveat).
function [nnzYBus, NYBus] = makeSparseYBus(busData, branchData)
  [iYBus, jYBus, valYBus] = constructSparseYBusTable(busData, branchData)
  [nnz, N] = sparmat([i, j, val])
function [deltaP, deltaQ] = computeMismatchesViaSparseYBus(nnzYBus, NYBus, ..)
function [nnzJ, NJ] = constructSparseJacobian(nnzYBus, NYBus, …)
[nnzL, NL, nnzU, NU] = factorizeSparseLU(nnzJ, NJ)
  updateSparseMatrix
  computeSparseTriangularProduct
Caveat: My own implementations were awkward. They were not adaptive to new inputs (i.e. they required all of the sparse inputs to be stated up front, no mechanism to make updates to existing sparse data structures). This later led to complications for performing even simple algorithms like LU Factorization (which is the last requirement as far as evaluation is concerned).

## Slide 10: Sample functions in modules
P3: NKGContinuationPowerFlow
  Dependencies: NKGPowerFlow: initializeVectors, computeBusInjections, solveUsingLU
  A few more functions, like PredictorFunction and CorrectorFunction (I just refactored a whole script by my project team mate, so for me it’s still in just one script, not too long.)
  plotCPFPlots
  displayCPFResults

## Slide 11: Sample functions in modules
P4: NKGStateEstimation
(My project partner completely did it.)
Requires Powerflow results from P1 for branch currents.
Likely requires using a lot of symbolic variables. Although he did it by literally writing out all of the derivative equations.
Then some addition of noise to the currents.
Then formation of H matrix, to be used in an iterative computation.

## Slide 12: Sample functions in modules
P5: NKGOptimalPowerFlow
Dependencies: NKGPowerFlow: initializeVectors, constructJacobian, solveForPowerFlow
Note: Usage of symbolic variables recommended for computation of derivatives and jacobians.
solveForEconomicDispatch for the first two scenarios
solveForOPF for the next two scenarios
  generateSymoblicPowerFlowEquations

## Slide 13: Expected Time for Completion ~ 135 hours You think we can do it faster?
Project Number | Project Name | Encountered or Perceived Toughness | Expect Time for Completion [hours] | Remarks | Prerequisites
1 | PowerFlow | Hard | 25 |  | -
2 | SparsePowerFlow | Very Hard | 50 | Most of the time spent in ideation. | -
3 | ContinuationPowerFlow | Medium | 10 |  | P1
4 | StateEstimation | Hard | 25 | Was never implemented by me. | P1
5 | OptimalPowerFlow | Hard | 25 | Has an easy part and a head-banging part. | P1

## Slide 14: Help yourself to my implementations Easy high-level overview of all projects can be obtained just through a quick glance at my implementations.
Have the GitHub Desktop app installed.
Have MATLAB 2023a installed. It helps to visualize desired outputs and check for function input arguments and outputs.
Clone my repo. It is fast and easy, plus I can help you if you haven’t done it before.
Run ee521_main.mlx and visualize required outputs, check out the functions and their arguments, etc. and save time.

## Slide 15: May our package be glorious!